## Slide 1: Modeling Neuromorphic Devices
Structure and Dynamics of Atomic Switch Networks
Ido Marcus
October 2016

## Slide 2: Neuromorphic Devices

## Slide 3: Neuromorphic Devices
What
Brain-like hardware
Why
Brain implants
Paradigm to succeed CMOS chips; neural computing, supercomputers
Artificial platform for brain research
possible future applications

## Slide 4: Atomic Switch Networks
Networks of self-assembled nanowires are a design scheme for neuromorphic devices
Resulting networks are densely interconnected
Devices can be probed while “working”
Demis et al., Nanotechnology (2015)

## Slide 5: Atomic Switch Networks (cont.)
The conductive (Ag) nanowires are coated with an insulating material
Metal-Insulator-Metal (MIM) interfaces are created at wire intersections. These are “Atomic Switches”
An atomic switch turns ON\OFF upon formation\dissolution of a conductive filament that bridges over the insulating gap
The electronically insulating gap is ionically conductive, so filament dynamics are due to ion migration
ON state
(Low resistance)
OFF state
(High resistance)
Coating
Ag
Ag
Ag
Coating

## Slide 6: Experimental Observations

## Slide 7: Atomic Switch Networks – Criticality and Fluctuation Scaling
Avizienis et al., PLoS ONE (2012)
ASN
Control

## Slide 8: Atomic Switch Networks – Criticality and Fluctuation Scaling (cont.)
Steig et al., Advanced Materials (2012)

## Slide 9: Atomic Switch Networks – Plasticity and Hysteretic Behavior
Nakayama et al., Unpublished

## Slide 10: Modeling

## Slide 11: Modeling - Motivation and Principles
Motivation:
  Using elementary circuit theory, reproduce dynamics measured experimentally
  Study the microscopic origin of the observed collective dynamics
  Study the extent of similarity to brain dynamics
Simulation stages:
Network generation
Equations extraction
Time evolution
Update switches
Solve circuit

## Slide 12: Network generation
Wires are scattered on a plane:
  Orientations and positions are uniformly distributed
  Lengths are sampled from a gamma distribution
Intersections (atomic switches) are labeled
Two wires are chosen as contacts to which a voltage bias is applied
Network generation
Equations extraction
Time evolution

## Slide 13: Equations extraction
Along each wire the potential is constant
Voltage drops occur across switches
For a given state of the switches, the voltage distribution can be found by solving Kirchhoff’s equations
Equations are obtained using a graph representation of the network
Network generation
Equations extraction
Time evolution

## Slide 14: Graph representation
Every wire is a vertex
Every switch (=intersection) is an edge
Network structure is represented with an adjacency matrix
  Graph is connected, undirected and unweighted
Network generation
Equations extraction
Time evolution
Notation vertices edges
Notation 𝑉 vertices 𝐸 edges
1
2
3
4
 | 1 | 2 | 3 | 4
1 | 0 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0
3 | 1 | 1 | 0 | 0
4 | 1 | 0 | 0 | 0
Atomic switch network
1
2
3
4
Equivalent graph
Graph’s adjacency matrix

## Slide 15: Kirchhoff’s Equations
The network is connected to a voltage source and a “tester” resistor:
The unknowns are voltage drops across the switches and the “tester”
Kirchhoff’s Current Law (KCL), that expresses charge conservation, yields linearly independent equations
  Equations are easy to extract, but
  Coefficients are time-dependent (conductance values of atomic switches)
Network generation
Equations extraction
Time evolution
Notation vertices edges
Notation 𝑉 vertices 𝐸 edges
Atomic Switch Network
“tester“ resistor
external voltage
contacts

## Slide 16: Kirchhoff’s Equations (cont.)
Kirchhoff’s Voltage Law (KVL), that expresses energy conservation, should yield linearly independent equations
But every cycle yields an equation, and usually . Huge redundancy!
Solution - Eulerean subgraphs form a vector space:
  (over 2-element field = symmetric difference as addition)
  The cycle space is spanned by a cycle basis, which can be found in polynomial time
  Coefficients are time-independent
Network generation
Equations extraction
Time evolution
Notation vertices edges
Notation 𝑉 vertices 𝐸 edges
Notes: A walk is an alternating sequence of vertices and edges, starting and ending at a vertex, in which each edge is adjacent in the sequence to its two endpoints.
A trail is a walk without repeated edges.
An Eulerian trail is a trail in a graph which visits every edge exactly once.
An Eulerian circuit is an Eulerian trail which starts and ends on the same vertex.
“Eulerian graph” has two common meanings. One meaning is a graph with an Eulerian circuit, and the other is a graph with every vertex of even degree. These definitions coincide for connected graphs.

## Slide 17: Kirchhoff’s Equations (summary)
(1
(V-1)
(1
(1
(
KCL
KVL
(
(
ext. source cycle
Update switches
Solve circuit
Network generation
Equations extraction
Time evolution

## Slide 18: Dynamics of an individual atomic switch
Every switch has an internal variable, , representing current length of filament
Switch is ON iff
Qualitative model for filament dynamics:
Update switches
Solve circuit
Network generation
Equations extraction
Time evolution
Voltage
Filament forming
No voltage
Filament dissolving
Opposite voltage

## Slide 19: Dynamics of an individual atomic switch (cont.)
Update switches
Solve circuit
Network generation
Equations extraction
Time evolution
When goes below

## Slide 20: Preliminary Results

## Slide 21: Static Solution
Voltage distribution, current paths, and dissipation can all be studied

## Slide 22
When the state of a switch changes, it affects the overall conductance
  Switches turn ON
  Switches are ON
    Bias is turned off, filaments are getting weak
  Switches turn OFF
  Switches are OFF
Bigger changes stem from collective switching of more switches
Dynamics
1
2
3
2a
4

## Slide 23: Fluctuation Scaling

## Slide 24: Fluctuation Scaling (cont.)
Under a DC bias, fluctuations in conductance show a 1/f noise pattern

## Slide 25: Random Squares Superimposed

## Slide 26: Random Gaussians Superimposed

## Slide 27: Fluctuation Scaling (cont.)
There is no characteristic time-scale for changes in the conductance

## Slide 28
Over time two clusters of switches are distinguished:
  A cluster with a majority of ON switches is formed between the contacts
  The other, with a majority of OFF switches, is “avoided” by the current
This process can be best seen in a movie
Clusters

## Slide 29
Formation of conductive paths
Power (logarithmic scale)
Time (sec)
Conductance (S)
Conductance as func. of time

## Slide 30: Conclusion
Elementary circuit analysis was combined with voltage-dependent dynamics of atomic switches
Overall behavior that had been experimentally observed was reproduced
  Time-dependent conductance
  Hysteresis
Underlying microscopic picture was elucidated
  Formation of conductive paths
  Clusters as emergent spatial pattern
Fluctuations are consistent with criticality

## Slide 31: Leads for Further Research
Origins of 1/f noise pattern:
  Different exponents for different states of the network (ON\OFF)?
Phase transition - first path of ON switches:
  Timing as function of difference from critical voltage
  Signal auto-corrolation as function of time
Big networks:
  Recurring spatiotemporal patterns
Modeling other systems (economics)

## Slide 32: Questions?
Thank you!